## Slide 1: STANDARD OPERATING PROCEDURE
FOR
HYDRAULIC PUMPS AND MOTORS

## Slide 2: MODEL ID:- A10VO SIZE:- 18,28,45,71,100,140CC
HYDRAULIC PUMP

## Slide 3: MODEL ID:- A10VO SIZE:- 18,28,45,71,100,140CC
Fit the hydraulic pump on the test bench
Connect all lines properly (Suction line, drain line, OC HP PUMP Line, OC feedback line)
Note:- The lines responsible for open circuit are marked above.

## Slide 4
Connection of all lines of the pump during air release from the pump.

## Slide 6: STANDARD OPERATING PROCEDURE
Main power MCB - ON/OFF
ON
OFF

## Slide 7: STANDARD OPERATING PROCEDURE
Fill the data in the software and select the required data in the panel.

## Slide 8: STANDARD OPERATING PROCEDURE
INCREASE RPM SWITCH
DIRECTION SELECTION SWITCH RH/LH
LOOP SELECTION SWITCH CLOSE/OPEN

## Slide 9: STANDARD OPERATING PROCEDURE
After this, start the engine and gradually increase the RPM to 1000.

## Slide 10: STANDARD OPERATING PROCEDURE
Before testing, increase pump speed and release air from the pump and Tank connect to feedback line during this time.
Check the load sensing pressure and set its pressure if necessary.
OC feedback line

## Slide 11: STANDARD OPERATING PROCEDURE
The pressure of load sensing and pressure compensator is checked by applying load.

## Slide 12: STANDARD OPERATING PROCEDURE
Load sensing setting
Pressure compensator setting(main pressure)
LS Connection line
PC (Main pressure)
LS (load sensing)

## Slide 13: STANDARD OPERATING PROCEDURE
Check the Pressure compensator pressure and set its pressure if necessary.
Whatever pressure we set, we do it according to the name plate.
For example:-
PC Setting – 250bar
LS Setting- 17bar

## Slide 14: STANDARD OPERATING PROCEDURE
Checking point in this model pumps:-
Pump Flow
LS pressure
Main pressure
Return flow
External leakage

## Slide 15: MODEL ID:- A11VO SIZE:- 40,60,75,95,130,145,190,260
HYDRAULIC PUMP OPEN CIRCUIT

## Slide 16: STANDARD OPERATING PROCEDURE
Fit the hydraulic pump on the test bench
Connect all lines properly (Suction line, drain line, OC HP PUMP Line, OC feedback line)
Note:- The lines responsible for open circuit are marked above.

## Slide 17: STANDARD OPERATING PROCEDURE
Main power MCB - ON/OFF
ON
OFF

## Slide 18: STANDARD OPERATING PROCEDURE
Fill the data in the software and select the required data in the panel.

## Slide 19: STANDARD OPERATING PROCEDURE
DIRECTION SELECTION SWITCH RH/LH
LOOP SELECTION SWITCH OPEN/CLOSE
INCREASE RPM SWITCH
PANEL ON/OFF SWITCH
EMERGENCY SWITCH

## Slide 20: STANDARD OPERATING PROCEDURE
After this, start the engine and gradually increase the RPM to 1000.

## Slide 21: STANDARD OPERATING PROCEDURE
Before testing, increase pump speed and release air from the pump and Tank connect to feedback line during this time.
Check the load sensing pressure and set its pressure if necessary.
OC FEEDBACK LINE

## Slide 22: STANDARD OPERATING PROCEDURE
The pressure of load sensing and pressure compensator is checked by applying load.

## Slide 23: STANDARD OPERATING PROCEDURE
Pressure compensator setting(main pressure)
Load sensing setting
PC (Main pressure)
LS (load sensing)
Torque setting
TORQUE ENGINE LOAD
LS Connection line

## Slide 24: STANDARD OPERATING PROCEDURE
Check the Pressure compensator pressure and set its pressure if necessary.
Whatever pressure we set, we do it according to the name plate.
For example:-

## Slide 25: STANDARD OPERATING PROCEDURE
Checking point in this model pumps:-
Pump Flow
LS pressure
Main pressure
Torque (Engine load)
Return flow
External leakage

## Slide 26: STANDARD OPERATING PROCEDURE
MODEL NO. :- 90 SERIES
SIZE:- 55,75,100,130,180,250
HYDRAULIC PUMP

## Slide 27: STANDARD OPERATING PROCEDURE
First of all, mount the hydraulic pump on the Test bench and connect all lines (Suction ,A /B pressure line, tank line)properly.
Main power MCB - ON/OFF
ON
OFF

## Slide 28: STANDARD OPERATING PROCEDURE
After that feed the data in software and select the data according to the pump in panel. For example:- select direction RH/LH, select loop Close ,Select extra charging ON/OFF

## Slide 29: STANDARD OPERATING PROCEDURE

## Slide 30: STANDARD OPERATING PROCEDURE
After this, start the engine and gradually increase the RPM to 1000.

## Slide 31: STANDARD OPERATING PROCEDURE
Before testing, increase pump speed and release air from the pump and gauge capillary connect to charging pressure checking point during this time.

## Slide 32: STANDARD OPERATING PROCEDURE